## Slide 1: Approaches to Hydroxylated Polyacenes I. David Reingold, Zachariah A. Page, and Anh Nguyen Department of Chemistry, Juniata College, Huntingdon, Pa 16652
Ultimate Research Goals
Synthesizing Building Blocks
Potential uses in OLED’s, photovoltaic cells, non-linear optics, and field effect transistors
Future Research
Future Research
Goals:
Reduce Reaction Time
Reduce Temperature
Minimal Solvent
Increase Yield
Potential Problems:
Polymerization
Decomposition
Isolate one-arm diester, then decarboxylate separately
Drip Ketal into base/DMM/ solvent mixture slowly to decrease polymerization.
Make tert-butyl esters
Base | Solvent | Temperature (⁰C) | Time (hr) | Yield (%)
DBU | NMP | 130 | 19.5 | 14
 | DBU (1 Eq H2O) | 100 | 23.5 | 30
 | Acetonitrile | 100 | 3 | none
KOH | NMP | Microwave: 300 W, 10 % | 5-15 min intervals for 3 hr | none (trouble decarbox.)
 | NMP | 110 | 6 days | 5
TEA | TEA | 120 | 8 days | 16
 | TEA | 130 | 5 days | 14
Base
Base
Michael-Claisen
Base | Solvent | Temperature (ºC) | Time (hr) | Yield (%)
DBU | NMP | 120 | 27.5 | 14
 | DBU (1 Eq H2O) | 95 | 24 | none
KOH | NMP | 95-120 | 7-27.5 | none
Cs2CO3 | NMP | 120 | 30 | none
KOC(CH3)3 | Acetonitrile | 80 | 22 | none
75 % Yield
Isolate and identify the other three isomers.
We believe that the methoxide leaving group may be reacting with our starting material, catalyzing the Baylis-Hillman reaction, and thus reducing our yield. So we would like to synthesize a reactant with a tert-butoxide leaving group, in order to prevent the nucleophilic reaction from happening.
This is a model of the reaction scheme to make polyhydroxy-kekulene. This is one “corner” of the molecule.
Model Condensation Reaction
1 eq
excess
IBD
MeOH
X-ray shows that isomer from THF is this one
Reingold, Butterfield, Daglen, Walters, Allen, Scheuring, Kratz, Gembicky, Baran, Tetrahedron Letters 2005, 46, 3835-3837.
Isomer obtained in NaH/THF
Diagnostic proton ~16 ppm
Isomers obtained in NaH/DBU
Isomers obtained in NaH/Pyridine
Four possible stereoisomers—ratio varies with conditions
Supported By
NSF REU
Chemistry
Simulation
Simulation
Dehydrogenation