## Slide 1
The reversible work, W, of forming a droplet within the supercooled LJ vapor
at kT/ε=0.8 and Pσ³/ɛ=0.01247 obtained from isothermal-isobaric Monte
Carlo simulations. The key features of the DFT predictions, such as the flat ridge
and limits of stability, are verified by the simulation.
The reversible work, W, of forming a droplet of given n and radius l within the
supercooled Lennard-Jones (LJ) vapor at kT/ε=0.8 and and ρσ³=0.01 obtained
from constrained density-functional theory (DFT). For n>15, each profile terminates
at a limit of stability. A flat ridge develops, i.e., maxima in W have the same values, for
larger droplet sizes. Hence, homogeneous droplet nucleation is more appropriately
described as an “activated instability”: once the droplets surmount the free energy
barrier the free energy surface serves to channel the embryos towards the stability
limits; the growth phase proceeds via a mechanism appropriate for an unstable fluid.
This is a new and intriguing picture of the molecular mechanism of droplet formation.
Activated Instability of Homogeneous Nucleation and Growth
David S. Corti, School of Chemical Engineering, Purdue University, West Lafayette , IN 47906
The reduced density, r*, versus Monte Carlo step after a cavity of radius l = 2.2s was placed within a superheated Lennard-Jones liquid. For the given temperature and pressure of the liquid, the cavity at the limit of stability has a radius of 1.8s. The introduction of a cavity beyond this critical size is found to generate an instability; the density begins to rapidly decrease, indicating that phase separation has begun to occur. These simulations confirm that the limits of stability predicted by the DFT method denote a real transition point between stable and unstable fluctuations within the superheated liquid.
Chart: 
l = 2.2s
r*